SOS INSTALLATION GUIDE



     The SOS  distribution  medium  contains  the  following
files:
               1)   INSTAL.DOC - this text
               2)   SOS.TSK
               3)   SOSBIG.TSK
               4)   SOS.HLP
               5)   SOSUG.DOC
               6)   RSX.RTS



     SOS runs as  a  non-priviledged  utility  program  from
account  [1,2].  Two versions of the task file are included:
SOS.TSK and SOSBIG.TSK.  SOS.TSK  is  an  overlayed  version
that  runs  in 11K, SOSBIG.TSK is not overlayed and requires
24K. The performance differs  only  slightly  during  normal
editing,  but the overlayed version has much higher overhead
during initialization and termination.  The choice of  which
to  use  is  dependent  on  whether  the limited resource is
memory or disk accesses.

     Two   documentation   files   are   included   on   the
distribution  tape.   A short help file, SOS.HLP, contains a
brief  description  of  the  commands,  and  is  printed  in
response  to  the  HELP  command  in  SOS.   A more complete
document, SOSUG.DOC, explains each command  in  more  detail
with all the options and parameters that are available.

     The program runs under the RSX run-time system;  a copy
is  included  in  this  kit  for  convenience.  If it is not
already installed on the system, do the following:
               RUN $PIP
               [0,1]RSX.RTS=DT:RSX.RTS/CO:T
               ^Z

and add the following to the START.CTL sequence:

               RUN $UTILTY
               ADD RSX
               ^Z


     The files should be  copied  into  the  system  library
account with the following sequence of commands:

               RUN $PIP
               [1,2]SOS.TSK=DT:SOS.TSK/CO:T
               [1,2]SOSBIG.TSK=DT:SOSBIG.TSK/CO:T
               [1,2]SOS.HLP=DT:SOS.HLP/CO:T

                    
                                                      Page 2



               [1,2]SOSUG.DOC=DT:SOSUG.DOC/CO:T
               =[1,2]SOS.TSK<104>/RE
               =[1,2]SOSBIG.TSK<104>/RE
               =[1,2]SOS.HLP<40>/RE
               =[1,2]SOSUG.DOC<40>/RE
               ^Z


     The  CCL  command  may  be  added  into  the  START.CTL
sequence:

               RUN $UTILTY
               CCL SOS=$SOS.TSK;0
                      or
               CCL SOS=$SOSBIG.TSK;0
               ^Z